## Slide 1
DEPARTMENT OF PHYSICS AND NANOTECHNOLOGY
SRM INSTITUTE OF SCIENCE AND TECHNOLOGY
18PYB103J –Semiconductor Physics
Module-V Lecture-9
Characterization Techniques-X-Ray Diffraction-Powder Method
18PYB103J Module-V Lecture-9

## Slide 2
18PYB103J Module-V Lecture-9
X-Ray Diffraction
X-ray diffraction is used for the complete determination of molecular structure of crystals.
Every lattice plane in a crystal behaves like diffraction grating, on the exposure of X-rays.
The position of the spectral lines when diffracted depends on the distance between successive lines; similarly the nature of the X-ray diffracted by a crystal is determined by the spacing between successive planes.

## Slide 3
18PYB103J Module-V Lecture-9

## Slide 4
18PYB103J Module-V Lecture-9
If a beam of monochromatic X-rays is incident on a crystal at an angle θ, some of the rays will be diffracted by the layers of atoms in the crystal.
The path length FC′D is larger than FCD by AC′B which is equal to 2AC′, and since AC′ = dsinθ, the path difference is 2dsinθ.
This difference in path length must be an integral number (n) of wavelengths (λ) for maximum diffraction of X-rays with destructive interference. Thus
nλ = 2dsinθ
which is the Bragg’s equation.
With the help of the Bragg’s equation it is possible to determine the spacing d between successive lattice planes, if λ is known and θ is measured.

## Slide 5
18PYB103J Module-V Lecture-9
The powder method:
A narrow beam of monochromatic X-rays fall on the finely powdered specimen to be examined, and the diffracted rays are passed on to a strip of film which almost completely surrounds the specimen.
The random orientation of crystals produces diffraction rings.
This method is commonly used for identification purposes by comparing the data with the standard files available.
For a cubic crystal the identification of lines in the powder photograph is simple compared to other types.

## Slide 6
18PYB103J Module-V Lecture-9
XRD is a nondestructive technique
To identify crystalline phases and orientation
To determine structural properties: Lattice parameters (10-
4Å), strain, grain size, phase composition.
To measure thickness of thin films and multi-layers
To determine atomic arrangement
Application of XRD