## Slide 1
18CSS201J
ANALOG AND DIGITAL ELECTRONICS

## Slide 2: UNIT 1 BJT- Bipolar Junction Transistor

## Slide 13: Transistor Configuration
The transistor has three terminals – emitter (E), base (B) and collector (C).
But in the circuit connections we need four terminals, two terminals for input and another two terminals for output. To overcome these problems we use one terminal as common for both input and output actions.
The behaviour of these three different configurations of transistors with respect to gain
Common Emitter (CE) Configuration: current gain and voltage gain
Common Collector (CC) Configuration: current gain but no voltage gain
Common Base (CB) Configuration: no current gain but voltage gain

## Slide 14: Common Emitter for NPN and PNP Transistor

## Slide 15: Common Emitter Input Characteristics

## Slide 16: COMMON EMITTER OUTPUT CHARACTERISTICS

## Slide 18: COMMON COLLECTOR FOR PNP AND NPN TRANSISTORS

## Slide 19: COMMON COLLECTOR INPUT CHARACTERISTICS

## Slide 20: COMMON COLLECTOR OUTPUT CHARACTERISTICS

## Slide 21: COMMON BASE FOR PNP AND NPN TRANSISTORS

## Slide 23: COMMON BASE INPUT CHARACTERISTICS

## Slide 24: COMMON BASE OUTPUT CHARACTERISTICS

## Slide 25
1. In a common base connection, current amplification factor is 0.9. If the emitter current is 1mA, determine the value of base current.
Solution :
2. In a common base connection, IC = 0.95 mA and IB = 0.05 mA. Find the value of α.
Solution :

## Slide 26
3. In a common base connection, IE = 1mA, IC = 0.95mA. Calculate the value of IB .
Solution :
4. In a common base connection, the emitter current is 1mA.
If the emitter circuit is open, the collector current is 50 μA.
Find the total collector current. Given that α = 0.92.
Solution :

## Slide 27
5. Calculate IE in a transistor for which β = 50 and IB = 20 μA.
Solution :

## Slide 28: COMPARISON OF CB,CE,CC

## Slide 29: RELATIONSHIP OF α,β, γ

## Slide 30: DC BIASING
Transistor Biasing is the process of setting a transistors DC operating voltage or current conditions to the correct level so that any AC input signal can be amplified correctly by the transistor

## Slide 31: DC BIASING

## Slide 32: DC BIASING
The correct operating point requires the selection of bias resistors and load resistors to provide the appropriate input current and collector voltage conditions.
The correct biasing point for a bipolar transistor, either NPN or PNP, generally lies somewhere between the two extremes of operation with respect to it being either “fully-ON” or “fully-OFF” along its DC load line. This central operating point is called the “Quiescent Operating Point”, or Q-point for short.

## Slide 33: Types of DC biasing
Fixed bias.
Collector-to-base bias.
Fixed bias with emitter resistor.
Voltage divider bias or potential divider.
Emitter bias.

## Slide 34: Uses of BJT
The bipolar junction transistor (BJT) is used in logic circuits.
The BJT is used as an oscillator.
It is used as an amplifier.
It is used as a multivibrator.
For wave shaping, it is used in clipping circuits.
Used as a detector or demodulator.
It is also used as a modulator.
Used in timer and time delay circuits.
It is used in electronics switch.
It is used in switching circuits.