## Slide 1: UNIT 1
Introduction to Analog Electronics
Session-2
Characteristics of JFET (Common Source, Common Drain and Common Gate configurations) and uses
Differences between BJT and JFET

## Slide 2: JUNCTION FIELD EFFECT TRANSISTOR (JFET)
(Image source: www.electronics-tutorials.ws)
CONSTRUCTION, TYPES & SYMBOLS
There are two types of JFET’s: n-channel and p-channel.
The n-channel is widely used.
Three terminals:
  Drain (D) and Source (S) are connected to n-channel
  Gate (G) is connected to the p-type material.
Gate is always reverse biased
Gate current, IG=0
BASICS

## Slide 3: JFET AMPLIFIER-CONFIGURATIONS
Common Source (CS) configuration (Good voltage amplifier)
    Mostly used, Similar to CE transistor
    Generally used in audio frequency amplifiers and in high input impedance pre-amplifier stages.
Common Drain (CD) configuration (Good voltage buffer)
    Source follower
    High input impedance and a low output impedance
    Approx. unity voltage gain-used in buffer amplifiers.
    referred to as “Common Drain” because there is no signal available at the drain connection.
Common Gate (CG) configuration (Good current buffer)
    Has a low input impedance, but a high output impedance.
    Applied in high frequency circuits or in impedance matching circuits where a low input impedance needs to be matched to a high output impedance
    Microphone amplifiers
1
2
3
BASICS

## Slide 4: COMMON SOURCE AMPLIFIER
In CS configuration, the input is given to the gate and the output is taken from the drain.
180 degree phase shift between input and output.
Features
Large voltage gain
Good voltage amplifier
Better transconductance amplifier
High input resistance
Medium / high output resistance
BASICS

## Slide 5: CONNECTION DIAGRAM FOR DETERMINING THE CS AMPLFIER CHARACTERISTICS
Drain Characteristics
Transfer characteristics

## Slide 6: CS AMPLIFIER CHARACTERISTICS
Drain or V-I characteristics
Output characteristics
Relationship between Drain current (ID) and Drain to source voltage (VDS) for different values of gate to source voltage (VGS)
Operation analysis includes
Without external bias: (VGS =0)
With external bias.
ID VS VDS FOR VGS = constant
VGS Depletion layer ID.

## Slide 7: CS AMPLIFIER CHARACTERISTICS
The transfer characteristics
The plot of the drain current Vs gate-source voltage for different values of drain to source voltage (VGS)
It is observed that the value of drain current varies inversely with respect to gate-source voltage when the drain-source voltage is constant.
The transfer characteristics is drawn between
input voltage and output current.
ID VS. VGS FOR VDS = constant

## Slide 8: CS AMPLIFIER CHARACTERISTICS
At the pinch-off point,
VGS at pinch-off is denoted as Vp
any further increase in VDS does not produce any increase in ID
ID is at saturation or maximum. It is referred to as IDSS.
(Image source: www.rezzonics.blogspot.com)

## Slide 9: CS AMPLIFIER CHARACTERISTICS
Important terms in JFET drain characteristics
Knee Point: Where the variation of drain current with drain-source voltage appears to be linear. But beyond this point, the linearity changes into a curve.
Channel Ohmic Region: The region to the left of the knee point in the characteristics curve.
Pinch-off point: The point in the curve beyond which the drain current will not increase further no matter how much we are increasing the drain to source voltage.
Pinch-off Voltage: The voltage at the pinch-off point is termed as pinch-off voltage because at this voltage, the current is completely turned to be constant.
Drain-Source Saturation Current: The drain to source saturation current is the current which becomes constant and enters into a saturation state.

## Slide 10: COMMON DRAIN JFET AMPLIFIER (Source follower)
Connect voltmeters and ammeters to measure the necessary voltages and currents (as explained in CS amplifier connections)
The transfer characteristics
The output characteristics

## Slide 11: COMMON GATE JFET AMPLIFIER-CHARACTERISTICS
The transfer characteristics
The output characteristics
Connect voltmeters and ammeters to measure the necessary voltages and currents (as explained in CS amplifier connections)

## Slide 12: COMPARISON BETWEEN BJT AND JFET
BJT | JFET
Bipolar device (current condition, by both types of carriers, i.e. majority and minority-electrons and hole). | Unipolar device (current conduction is only due to one type of majority carrier either electron or hole).
The operation depends on the injection of minority carries across a forward biased junction. | The operation depends on the control of a junction depletion width under reverse bias.
Current controlled device. The base current controls the output current. | Voltage controlled device. The gate voltage controls output current.
High noise level. (current conduction through junctions) | Low noise level. ( current conduction is through n-channel or p-channel and no junction crossing)
Low input impedance (due to forward bias at input side). | High input impedance (due to reverse bias).
Gain is characterized by voltage gain. | Gain is characterised by transconductance.
Low thermal stability. (positive temperature coefficient at high current levels lead to thermal breakdown) | Better thermal stability.(NTC at high current levels prevent thermal breakdown)
Cheaper | Relatively costly

## Slide 13: REVIEW QUESTIONS
Source follower is a circuit that provides_________
In CS amplifier, the drain-source current is largest when the gate-source voltage VGS is____
Which JFET amplifier configuration is used in microphone amplifiers?
JFET is a ___ controlled device