## Slide 1: Accident prevention technique
JOB safety analysis

## Slide 2: Techniques of accident prevention
Objective : control hazards at work, so as to reduce or eliminate accidents
3 steps in management of hazards:
Identification
Evaluation or assessment
Control
Within the organization, several ways by which hazards may be identified:
1. workplace inspections
2. management/worker discussions
3. independent audits
4. job safety analysis
5. hazard and operability studies

## Slide 4: OBJECTIVES
Understand the benefits of JSAs
Understand the purpose and function
Know the developmental process
Determine when to develop
Identify responsibilities

## Slide 5
What is job safety analysis?

## Slide 6: DEFINITION
JSA: A systematic method of identifying hazards & control measures to safely perform a specific task.
Notes: READ THE SLIDE

## Slide 7: BENEFITS OF JSAs
Training of new employees
Accident investigation tool
Supervisor evaluation tool
Consistency in training
Injury reduction

## Slide 8: Factors to be considered in setting a priority for analysis of jobs include:
 Accident frequency and severity: jobs where accidents occur frequently or where they occur infrequently but result in disabling injuries.
 Potential for severe injuries or illnesses: the consequences of an accident, hazardous condition, or exposure to harmful substance are potentially severe.
 Newly established jobs: due to lack of experience in these jobs, hazards may not be evident or anticipated.
 Modified jobs: new hazards may be associated with changes in job procedures.

## Slide 9: General accepted measures
Eliminate the hazard
Contain the Hazard
Revise Work Procedures
Reduce the Exposure

## Slide 10: THE PROCESS
JSA:
  Breaking down a job into steps
  Identifying safety hazards at each step
  Developing safe job procedures for each step

## Slide 11: JSA PROCEDURE
STEP 1:
  Select the job
    JSA’s need to be completed when the following occurs: Fatalities, accident trends, new procedure or new job, or new equipment that has a hazard associated with it.
    You can also perform JSAs based on Freq of Accidents, Severity of Accidents, Potential Severity.

## Slide 12: JSA PROCEDURE
STEP 2:
    Perform the Analysis Who is the most qualified person to conduct the JSA– Supervisors of the department where the jobs are performed.
    Employees that actually perform the work are also qualified to conduct the JSA. Getting employees involved in the process helps to “sell the process”.
    Observe performance of task, record each step, review the steps with employee who performed task.
    Avoid common errors
    Making the breakdown too detailed so that an unnecessarily large number of steps result or
    2. Making the job breakdown so general that the basic steps are not distinguishable.
    3. Make sure steps are in correct order.
    TIP
    The wording for each step should begin with an action word such as “remove”, “open”, “lift”, etc.

## Slide 13
STEP 3:
    IDENTIFY HAZARDS Is there danger of striking against, being struck by, or otherwise making injurious contact with an object?
    Can the employee be caught in ,caught by or between the objects?
    Is there a potential for a slip or trip?
    Can an employee strain himself/herself by pushing, pulling, lifting, bending, or twisting?
    Is the environment hazardous to one’s health (toxic gas, vapor, mist, fumes, dust, heat or radiation)?
PROCEDURE Cont’d

## Slide 14: PROCEDURE Cont’d
STEP 4:
    DEVELOP SOLUTIONS - Find a new way to do the job (determine the goal of the operation and select the safest method)
    Change the physical conditions that created the hazard ( such as tools, equipment, work area layout)
    Change the work procedure to eliminate the hazard
    Reduce the frequency of its performance Implement administrative controls-Job Rotation
    Use personal protective equipment to protect the employee.

## Slide 15: PROCEDURE Cont’d
STEP 5:
    Conduct a Follow-up Analysis: Supervisors should observe employees as they perform at least one job per month for which a JSA have been completed.
    Purpose of the Observations: To determine if employees are following the job procedures as developed on the JSA.

## Slide 16: PROCEDURE Cont’d
STEP 6:
Use of the Job Safety Analysis: Document use of. The JSA provides a learning opportunity for supervisor and employees.
New employees should be trained using the JSA and ALL employees should be trained at least annually.
JSA used for training on infrequent task performed by employees. Document use of.
The JSA is an incident/accident investigation tool. If a JSA has been completed on a task in which an incident/accident has occurred, the JSA should be reviewed & modified as needed.

## Slide 17: PROCEDURE Cont’d
STEP 7:
    Recordkeeping:JSA should be maintained in the department where they were created.
    JSA should be readily accessible to employees.
    Maintain inventory list of JSA’s that have been developed. The JSA index should include the name of task, date the JSA was completed & the date the JSA was last revised.

## Slide 19: REVIEW JSAs...
During an accident/incident investigation process
Prior to conducting training
When work processes are changed or modified
JSAs
Notes: If a job process is changed dramatically, it should be discussed with all personnel involved to determine the possible consequences of the changes.
Such discussions check the accuracy of the job safety analysis and involve personnel in the effort to reduce job hazards.

## Slide 22
accident prevention