## Slide 1: DOW FIRE AND EXPLOSION INDEX
Unit-4

## Slide 2: DOW FIRE AND EXPLOSION INDEX
The hazard classification guide developed by the Dow Chemical Company and published by the American Institute of Chemical Engineering, Dow (1987)
The method of evaluating the potential risk from a process, and assessing the potential loss.
A numerical "Fire and explosion index" (F & El) is calculated, based on the nature of the process and the properties of the process materials. The larger the value of the F & El, the more hazardous the process

## Slide 3: Dow Fire and Explosion Index
To assess the potential hazard of a new plant, the index can be calculated after the Piping and Instrumentation and equipment layout diagrams have been prepared.
In earlier versions of the guide the index was then used to determine what preventative and protection measures were needed.
In the current version the preventative and protection measures, that have been incorporated in the plant design to reduce the hazard-are taken into account when assessing the potential loss; in the form of loss control credit factors.

## Slide 4: Calculation of the Dow F & El
The first step is to identify the units that would have the greatest impact on the magnitude of any fire or explosion. The index is calculated for each of these units.
The basis of the F & El is a Material Factor (MF). The MF is then multiplied by a Unit Hazard Factor, F3, to determine the F & El for the process unit.
The Unit Hazard factor is the product of two factors which take account of the hazards inherent in the operation of the particular process unit: the general and special process hazards
C1- process control credit factor
C2 – Material Isolation credit factor
C3 – Fire protection credit factor

## Slide 5: Material factor
The material factor is a measure of the intrinsic rate of energy release from the burning, explosion, or other chemical reaction of the material. Values for the MF for over 300 of the most commonly used substances are given in the guide.

## Slide 6: General process hazards The general process hazards are factors that play a primary role in determining the magnitude of the loss following an incident.
A. Exothermic chemical reactions: the penalty varies from 0.3 for a mild exotherm, such as hydrogenation, to 1.25 for a particularly sensitive exotherm, such as nitration.
B. Endothermic processes', a penalty of 0.2 is applied to reactors, only. It is increased to 0.4 if the reactor is heated by the combustion of a fuel.
C. Materials handling and transfer: this penalty takes account of the hazard involved in the handling, transfer and warehousing of the material.
D. Enclosed or indoor process units: accounts for the additional hazard where ventilation is restricted.
E. Access of emergency equipment: areas not having adequate access are penalised. Minimum requirement is access from two sides.
F. Drainage and spill control: penalises design conditions that would cause large spills of flammable material adjacent to process equipment; such as inadequate design of drainage.

## Slide 7: Special process hazards
The special process hazards are factors that are known from experience to contribute to the probability of an incident involving loss.
Twelve factors are listed on the calculation form
A. Toxic materials
B. Sub-atmospheric pressure
C. Operation in or near flammable range
D. Dust explosion
E. Relief pressure
F. Low temperature
G. Quantity of flammable material
H. Corrosion and erosion
I. Leakage—joints and packing
J. Use of fired heaters:
K. Hot oil heat exchange system:
L. Rotating equipment:

## Slide 8: Potential loss
The procedure for estimating the potential loss
The first step is to calculate the Damage factor for the unit. The Damage factor depends and the value of the Material factor and the Process unit hazards factor
An estimate of the replacement value of the equipment within the exposed area is then made, and combined with by the damage factor to estimate the Base maximum probable property damage (Base MPPD).
The Maximum probable property damage (MPPD) is then calculated by multiplying the Base MPPD by a Credit control factor.
The MPPD is used to predict the maximum number of days which the plant will be down for repair, the Maximum probable days outage (MPDO).
The MPDO is used to estimate the financial loss due to the lost production: the Business interruption (Bl). The financial loss due to lost business opportunity can often exceed the loss from property damage.