## Slide 1: Introduction to Digital Filters

## Slide 2: Digital Filters
Introduction
Types of filters
  FIR filters
  IIR filters
Choosing between FIR and IIR filters
Filter design steps

## Slide 3: Introduction
A digital filter is a mathematical algorithm implemented in hardware and/or software that operates on a digital input signal to produce a digital output signal for the purpose of achieving a filtering objective.
Digital filters operate on digitized analog signals or just numbers, representing some variable, stored in a computer memory.
Fig 1: A simplified block diagram of a real-time digital filter with analog input and output signals1

## Slide 4
Digital filters are used in applications like data compression, biomedical signal processing, speech and image processing, data transmission, digital audio, telephone echo cancellation etc.
Some advantages of digital filters over analog filters
  Truly linear phase response.
  Performance does not vary with environmental changes, for example thermal variations.
  The frequency response can be automatically adjusted if the filter is implemented using a programmable processor.
  Digital filters can be used at very low frequencies.

## Slide 5
Main disadvantages of digital filters over analog filters
  Speed limitation: The maximum bandwidth of signals that digital filters can handle, in real time, is much lower than for analog signals.
  Finite wordlength effects: Digital filters are subject to noises like ADC noise and roundoff noise that could lead to instability.
  Long design and development times: The design and development times for digital filters, especially hardware development, can be much longer than for analog filters.

## Slide 6: Types of filters
Digital filters
FIR IIR
A digital filter in general can be represented by its impulse response, h(k) (k=0,1,..) as in the following figure:
Fig 2: A conceptual representation of a digital filter1

## Slide 7
The input and output signals to the filter are related by the convolution sum:

y(n)   h(k )x(n  k )
k 0
N 1
y(n)   h(k )x(n  k )
k 0
IIR (1)
FIR (2)
Because of the infinite length of the impulse response of the IIR filter, the IIR filtering equation can be expressed in a recursive form as:
 N M
y(n)   h(k )x(n  k )  bk x(n  k )   ak y(n  k ) (3)
k 0 k 0 k 1
where ak and bk are the coefficients of the filter.

## Slide 8
We note that in eqn (3), the current output sample, y(n), is a function of past outputs as well as present and past input samples, that is the IIR is a feedback system of some sort.
In the FIR equation, the current output sample, y(n), is a function only of past and present values of the input.
The transfer functions of FIR and IIR filters:
N 1
H (z)   h(k )z k k 0
FIR (4)
M
1  ak z k k 1
H (z)  k 0
N
bk z k
IIR
(5)

## Slide 9: Choosing between FIR and IIR filters
Can have exactly linear phase response, i.e. do not distort the phase of the signal. | The phase responses are nonlinear, especially at the band edges.
FIR filters realized non- recursively are always stable. | The stability of IIR filters cannot be guaranteed.
The effects of using limited number of bits to implement filters are less severe. | The effects like roundoff noise and coefficient quantization errors are more severe.
Require more coefficients for sharp cutoff filters. | Less coefficients and thus less processing time and storage.
No analog counterpart, but, easier to synthesize filters with arbitrary frequency responses. | Analog filters can be readily transformed into equivalent IIR digital filters.
Algebraically more difficult to synthesize if CAD support is not available. | Less difficult to synthesize.
FIR filters IIR filters
1.
2.
3.
4.
5.
6.

## Slide 10
Thus, a broad guideline on when to use FIR or IIR would be as follows:
  Use IIR when the only important requirements are sharp cutoff filters and high throughput, as IIR filters will give fewer coefficients than FIR.
  Use FIR if the number of filter coefficients is not too large and, in particular, if little or no phase distortion is desired.