## Slide 1: 21CSS201T COMPUTER ORGANIZATION AND ARCHITECTURE UNIT-1

## Slide 2: Computer Architecture Objectives
Know the difference between computer organization and computer architecture.
Understand units of measure common to computer systems
Appreciate the evolution of computers.
Understand the computer as a layered system.
Be able to explain the von Neumann architecture and the function of basic computer components.

## Slide 3: COMPUTER ARCHITECTURE AND ORGANIZATION OVERVIEW
A modern computer is an electronic, digital, general purpose computing machine that automatically follows a step-by-step list of instructions to solve a problem. This step-by step list of instructions that a computer follows is also called an algorithm or a computer program.
Why to study computer organization and architecture?
  Design better programs, including system software such as compilers, operating systems, and device drivers.
  Optimize program behavior.
  Evaluate (benchmark) computer system performance.
  Understand time, space, and price tradeoffs.
Computer organization
  Encompasses all physical aspects of computer systems.
  E.g., circuit design, control signals, memory types.
  How does a computer work?

## Slide 4
Focuses on the structure(the way in which the components are interrelated) and behavior of the computer system and refers to the logical aspects of system implementation as seen by the programmer
Computer architecture includes many elements such as
  instruction sets and formats, operation codes, data types, the number and types of registers, addressing modes, main memory access methods, and various I/O mechanisms.
The architecture of a system directly affects the logical execution of programs.
The computer architecture for a given machine is the combination of its hardware components plus its instruction set architecture (ISA).
The ISA is the interface between all the software that runs on the machine and the hard
Studying computer architecture helps us to answer the question: How do I design a computer?
COMPUTER ARCHITECTURE AND ORGANIZATION OVERVIEW

## Slide 5
In the case of the IBM, SUN and Intel ISAs, it is possible to purchase processors which execute the same instructions from more than one manufacturer
All these processors may have quite different internal organizations but they all appear identical to a programmer, because their instruction sets are the same
Organization & Architecture enables a family of computer models
Same Architecture, but with differences in Organization
Different price and performance characteristics
When technology changes, only organization changes.
This gives code compatibility (backwards)
COMPUTER ARCHITECTURE AND ORGANIZATION OVERVIEW

## Slide 6: COMPUTER COMPONENTS
At the most basic level, a computer is a device consisting of 3 pieces
  A processor to interpret and execute programs
  A memory ( Includes Cache, RAM, ROM) to store both data and program instructions
  A mechanism for transferring data to and from the outside world.
    I/O to communicate between computer and the world
    Bus to move info from one computer component to another

## Slide 7: Contd..
Computers with large main memory capacity can run larger programs with greater speed than computers having small memories.
RAM is an acronym for random access memory. Random access means that memory contents can be accessed directly if you know its location.
Cache is a type of temporary memory that can be accessed faster than RAM.

## Slide 8: 1ST GENERATION COMPUTERS
  Used vacuum tubes for logic and storage (very little storage available)
  A vacuum-tube circuit storing 1 byte
  Programmed in machine language
  Often programmed by physical connection (hardwiring)
  Slow, unreliable, expensive
  The ENIAC – often thought of as the first programmable electronic computer – 1946
  17468 vacuum tubes, 1800 square feet, 30 tons

## Slide 9: 2nd Generation Computers
  Transistors replaced vacuum tubes
  Magnetic core memory introduced
  Changes in technology brought about cheaper and more reliable computers (vacuum tubes were very unreliable)
  Because these units were smaller, they were closer together providing a speedup over vacuum tubes
  Various programming languages introduced (assembly, high-level)
  Rudimentary OS developed
  The first supercomputer was introduced, CDC 6600 ($10 million)

## Slide 10: 3RD GENERATION COMPUTERS INTEGRATED CIRCUIT (IC)
The ability to place circuits onto silicon chips
  Replaced both transistors and magnetic core memory
  Result was easily mass-produced components reducing the cost of computer manufacturing significantly
  Also increased speed and memory capacity
  Computer families introduced
  Minicomputers introduced
  More sophisticated programming languages and OS developed
  Popular computers included PDP-8, PDP-11, IBM 360 and Cray produced their first supercomputer, Cray-1
  Silicon chips now contained both logic (CPU) and memory
  Large-scale computer usage led to time-sharing OS

## Slide 11: 4th Generation Computers 1971-Present: Microprocessors
Miniaturization took over
  From SSI (10-100 components per chip) to
  MSI (100-1000), LSI (1,000-10,000), VLSI (10,000+)
Thousands of ICs were built onto a single silicon chip(VLSI), which allowed Intel, in 1971, to
  create the world’s first microprocessor, the 4004, which was a fully functional, 4-bit system that ran at 108KHz.
  Intel also introduced the RAM chip, accommodating 4Kb of memory on a single chip. This allowed computers of the 4th generation to become smaller and faster than their solid-state predecessors
  Computers also saw the development of GUIs, the mouse and handheld devices

## Slide 12: The Computer Level Hierarchy
Through the principle of abstraction, we can imagine the machine to be built from a hierarchy of levels, in which each level has a specific function and exists as a distinct hypothetical Machine
Abstraction is the ability to focus on important aspects of a situation at a higher level while ignoring the underlying complex details
We call the hypothetical computer at each level a virtual machine.
Each level’s virtual machine executes its own particular set of instructions, calling upon machines at lower levels to carry out the tasks when necessary

## Slide 13: The Computer Level Hierarchy
Level 6: The User Level
Composed of applications and is the level with which everyone is most familiar.
At this level, we run programs such as word processors, graphics packages, or games.
The lower levels are nearly invisible from the User Level.

## Slide 14: The Computer Level Hierarchy
Level 5: High-Level Language Level
  The level with which we interact when we write programs in languages such as C, Pascal, Lisp, and Java
  These languages must be translated to a language the machine can understand. (using compiler / interpreter)
  Compiled languages are translated into assembly language and then assembled into machine code. (They are translated to the next lower level.)
  The user at this level sees very little of the lower levels

## Slide 15: The Computer Level Hierarchy
Level 4: Assembly Language Level
  Acts upon assembly language produced from Level 5, as well as instructions programmed directly at this level
  As previously mentioned, compiled higher-level languages are first translated to assembly, which is then directly translated to machine language. This is a one-to-one translation, meaning that one assembly language instruction is translated to exactly one machine language instruction.
  By having separate levels, we reduce the semantic gap between a high-level language and the actual machine language

## Slide 16: The Computer Level Hierarchy
Level 3: System Software Level
  deals with operating system instructions.
  This level is responsible for multiprogramming, protecting memory, synchronizing processes, and various other important functions.
  Often, instructions translated from assembly language to machine language are passed through this level unmodified

## Slide 17: The Computer Level Hierarchy
Level 2: Machine Level
  Consists of instructions (ISA)that are particular to the architecture of the machine
  Programs written in machine language need no compilers, interpreters, or assemblers
Level 1: Control Level
  A control unit decodes and executes instructions and moves data through the system.
  Control units can be microprogrammed or hardwired
  A microprogram is a program written in a low-level language that is implemented by the hardware.
  Hardwired control units consist of hardware that directly executes machine instruction

## Slide 18: The Computer Level Hierarchy
Level 0: Digital Logic Level
  This level is where we find digital circuits (the chips)
  Digital circuits consist of gates and wires.
  These components implement the mathematical logic of all other levels

## Slide 19: The Von Neumann Architecture
Named after John von Neumann, Princeton, he designed a computer architecture whereby data and instructions would be retrieved from memory, operated on by an ALU, and moved back to memory (or I/O)
This architecture is the basis for most modern computers (only parallel processors and a few other unique architectures use a different model)

## Slide 20: The Von Neumann Architecture
There is a single pathway used to move both data and instructions between memory, I/O and CPU
  the pathway is implemented as a bus
  the single pathway creates a bottleneck
    known as the von Neumann bottleneck
  A variation of this architecture is the Harvard architecture which separates data and instructions into two pathways
  Another variation, used in most computers, is the system bus version in which there are different buses between CPU and memory and memory and I/O

## Slide 21: Fetch-execute cycle
The von Neumann architecture operates on the fetch-execute cycle
  Fetch an instruction from memory as indicated by the Program Counter register
  Decode the instruction in the control unit
  Data operands needed for the instruction are fetched from memory
  Execute the instruction in the ALU storing the result in a register
  Move the result back to memory if needed

## Slide 22: THE VON NEUMANN MODEL
This is a general depiction of a von Neumann system:
These computers employ a fetch-decode-execute cycle to run programs as follows . . .

## Slide 23: THE VON NEUMANN MODEL
The control unit fetches the next instruction from memory using the program counter to determine where the instruction is located

## Slide 24: THE VON NEUMANN MODEL
The instruction is decoded into a language that the ALU can understand.

## Slide 25: THE VON NEUMANN MODEL
Any data operands required to execute the instruction are fetched from memory and placed into registers within the CPU.

## Slide 26: THE VON NEUMANN MODEL
The ALU executes the instruction and places results in registers or memory.

## Slide 27: Non-Von Neumann Models
Conventional stored-program computers have undergone many incremental improvements over the years
  specialized buses
  floating-point units
  cache memories
But enormous improvements in computational power require departure from the classic von Neumann architecture
  Adding processors is one approach

## Slide 28: Non-Von Neumann Models
In the late 1960s, high-performance computer systems were equipped with dual processors to increase computational throughput.
In the 1970s supercomputer systems were introduced with 32 processors.
Supercomputers with 1,000 processors were built in the 1980s.
In 1999, IBM announced its Blue Gene system containing over 1 million processors.

## Slide 29: Introduction to Number System and Logic Gates
  Number Systems- Binary, Decimal, Octal, Hexadecimal
  Codes- Grey, BCD,Excess-3,
  ASCII, Parity
  Binary Arithmetic- Addition, Subtraction, Multiplication, Division using Sign Magnitude
  1’s compliment, 2’s compliment,
  BCD Arithmetic;
  Logic Gates-AND, OR, NOT, NAND,
  NOR, EX-OR, EX-NOR

## Slide 30: Digital System
Takes a set of discrete information inputs and discrete internal information (system state) and generates a set of discrete information outputs.
System State
Discrete
Information
Processing
System
Discrete
Inputs
Discrete
Outputs

## Slide 31: Types of Digital Systems
No state present
  Combinational Logic System
  Output = Function(Input)
State present
  State updated at discrete times
  => Synchronous Sequential System
  State updated at any time
  =>Asynchronous Sequential System
  State = Function (State, Input)
  Output = Function (State) or Function (State, Input)

## Slide 32: Digital System Example
A Digital Counter (e. g., odometer):
1
3
0
0
5
6
4
Count Up
Reset
Inputs:
Count Up, Reset
Outputs:
Visual Display
State:
"Value" of stored digits
Synchronous or Asynchronous?

## Slide 33: A Digital Computer Example
Synchronous or Asynchronous?
Inputs: Keyboard, mouse, modem, microphone
Outputs: CRT, LCD, modem, speakers
Notes: Answer: Part of specification for a PC is in MHz. What does that imply? A clock which defines the discrete times for update of state for a synchronous system. Not all of the computer may be synchronous, however.

## Slide 34: Signal
An information variable represented by physical quantity.
For digital systems, the variable takes on discrete values.
Two level, or binary values are the most prevalent values in digital systems.
Binary values are represented abstractly by:
  digits 0 and 1
  words (symbols) False (F) and True (T)
  words (symbols) Low (L) and High (H)
  and words On and Off.
Binary values are represented by values or ranges of values of physical quantities

## Slide 35: Signal Examples Over Time
Analog
Asynchronous
Synchronous
Time
Continuous in value & time
Discrete in value & continuous in time
Discrete in value & time
Digital

## Slide 36: Binary Values: Other Physical Quantities
What are other physical quantities represent 0 and 1?
  CPU Voltage
  Disk
  CD
  Dynamic RAM
Magnetic Field Direction
Surface Pits/Light
Electrical Charge

## Slide 37: Number Systems Representation
Positive radix, positional number systems
A number with radix r is represented by a string of digits: An - 1An - 2 … A1A0 . A- 1 A- 2 … A- m + 1 A- m in which 0 £ Ai < r and . is the radix point.
The string of digits represents the power series:
(
)
(
)
(Number)r
=
å
å
+
j = - m
j
j
i
i = 0
i
r
A
r
A
(Integer Portion)
+
(Fraction Portion)
i = n - 1
j = - 1

## Slide 38: Number Systems – Examples
 | General | Decimal | Binary
Radix (Base) | r | 10 | 2
Digits | 0 => r - 1 | 0 => 9 | 0 => 1
0 1 2 3 Powers of 4 Radix 5 -1 -2 -3 -4 -5 | r0 r1 r2 r3 r4 r5 r -1 r -2 r -3 r -4 r -5 | 1 10 100 1000 10,000 100,000 0.1 0.01 0.001 0.0001 0.00001 | 1 2 4 8 16 32 0.5 0.25 0.125 0.0625 0.03125

## Slide 39: Special Powers of 2
210 (1024) is Kilo, denoted "K"
220 (1,048,576) is Mega, denoted "M"
230 (1,073, 741,824)is Giga, denoted "G"

## Slide 40: Positive Powers of 2
Useful for Base Conversion
Exponent
Value
Exponent
Value
0
1
11
2,048
1
2
12
4,096
2
4
13
8,192
3
8
14
16,384
4
16
15
32,768
5
32
16
65,536
6
64
17
131,072
7
128
18
262,144
19
524,288
20
1,048,576
21
2,097,152
8
256
9
512
10
1024

## Slide 41: Converting Binary to Decimal
To convert to decimal, use decimal arithmetic to form S (digit × respective power of 2).
Example:Convert 110102 to N10:
Notes: Powers of 2: 43210
110102 =>
1 X 24 = 16
+ 1 X 23 = 8
+ 0 X 22 = 0
+ 1 X 21 = 2
+ 0 X 20 = 0
2610

## Slide 42: Converting Decimal to Binary
Method 1
  Subtract the largest power of 2 (see slide 14) that gives a positive remainder and record the power.
  Repeat, subtracting from the prior remainder and recording the power, until the remainder is zero.
  Place 1’s in the positions in the binary result corresponding to the powers recorded; in all other positions place 0’s.
Example: Convert 62510 to N2
Notes: 625 – 512 = 113 => 9
113 – 64 = 49 => 6
49 – 32 = 17 => 5
17 – 16 = 1 => 4
1 – 1 = 0 => 0
Placing 1’s in the result for the positions recorded and 0’s elsewhere,
9 8 7 6 5 4 3 2 1 0
1 0 0 1 1 1 0 0 0 1

## Slide 43: Commonly Occurring Bases
Name
Radix
Digits
Binary
2
0,1
Octal
8
0,1,2,3,4,5,6,7
Decimal
10
0,1,2,3,4,5,6,7,8,9
Hexadecimal
16
0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
The six letters (in addition to the 10
integers) in hexadecimal represent:
Notes: Answer: The six letters A, B, C, D, E, and F represent the digits for values
10, 11, 12, 13, 14, 15 (given in decimal), respectively, in hexadecimal.
Alternatively, a, b, c, d, e, f are used.

## Slide 44: Numbers in Different Bases
Decimal
(Base 10)
Binary
(Base 2)
Octal
(Base 8)
Hexa
decimal
(Base 16)
00
00000
00
00
01
00001
01
01
02
00010
02
02
03
00011
03
03
04
00100
04
04
05
00101
05
05
06
00110
06
06
07
00111
07
07
08
01000
10
08
09
01001
11
09
10
01010
12
0A
11
0101
1
13
0B
12
01100
14
0C
13
01101
15
0D
14
01110
16
0E
15
01111
17
0F
16
10000
20
10
Good idea to memorize!

## Slide 45: Conversion Between Bases
Method 2
To convert from one base to another:
1) Convert the Integer Part
2) Convert the Fraction Part
3) Join the two results with a radix point

## Slide 46: Conversion Details
To Convert the Integral Part:
  Repeatedly divide the number by the new radix and save the remainders. The digits for the new radix are the remainders in reverse order of their computation. If the new radix is > 10, then convert all remainders > 10 to digits A, B, …
To Convert the Fractional Part:
  Repeatedly multiply the fraction by the new radix and save the integer digits that result. The digits for the new radix are the integer digits in order of their computation. If the new radix is > 10, then convert all integers > 10 to digits A, B, …

## Slide 47: Example: Convert 46.687510 To Base 2
Convert 46 to Base 2
Convert 0.6875 to Base 2:
Join the results together with the radix point:
Notes: Answer 1: Converting 46 as integral part: Answer 2: Converting 0.6875 as fractional part:
46/2 = 23 rem = 0 0.6875 * 2 = 1.3750 int = 1
23/2 = 11 rem = 1 0.3750 * 2 = 0.7500 int = 0
11/2 = 5 remainder = 1 0.7500 * 2 = 1.5000 int = 1
5/2 = 2 remainder = 1 0.5000 * 2 = 1.0000 int = 1
2/2 = 1 remainder = 0 0.0000
1/2 = 0 remainder = 1 Reading off in the forward direction: 0.10112
Reading off in the reverse direction: 1011102
Answer 3: Combining Integral and Fractional Parts:
101110. 10112

## Slide 48: Additional Issue - Fractional Part
Note that in this conversion, the fractional part became 0 as a result of the repeated multiplications.
In general, it may take many bits to get this to happen or it may never happen.
Example: Convert 0.6510 to N2
  0.65 = 0.1010011001001 …
  The fractional part begins repeating every 4 steps yielding repeating 1001 forever!
Solution: Specify number of bits to right of radix point and round or truncate to this number.

## Slide 49: Checking the Conversion
To convert back, sum the digits times their respective powers of r.
From the prior conversion of 46.687510
1011102 = 1·32 + 0·16 +1·8 +1·4 + 1·2 +0·1
= 32 + 8 + 4 + 2
= 46
0.10112 = 1/2 + 1/8 + 1/16
= 0.5000 + 0.1250 + 0.0625
= 0.6875

## Slide 50: A Final Conversion Note
You can use arithmetic in other bases if you are careful:
Example: Convert 1011102 to Base 10 using binary arithmetic:
  Step 1 101110 / 1010 = 100 r 0110
  Step 2 100 / 1010 = 0 r 0100
  Converted Digits are 01002 | 01102
  or 4 6 10

## Slide 51: Binary Numbers and Binary Coding
Flexibility of representation
  Within constraints below, can assign any binary combination (called a code word) to any data as long as data is uniquely encoded.
Information Types
  Numeric
    Must represent range of data needed
    Very desirable to represent data such that simple, straightforward computation for common arithmetic operations permitted
    Tight relation to binary numbers
  Non-numeric
    Greater flexibility since arithmetic operations not applied.
    Not tied to binary numbers

## Slide 52: Non-numeric Binary Codes
Given n binary digits (called bits), a binary code is a mapping from a set of represented elements to a subset of the 2n binary numbers.
Example: A binary code for the seven colors of the rainbow
Code 100 is not used
Binary Number
000
001
010
011
101
110
111
Color
Red
Orange
Yellow
Green
Blue
Indigo
Violet

## Slide 53: Number of Bits Required
Given M elements to be represented by a binary code, the minimum number of bits, n, needed, satisfies the following relationships:
    2n > M > 2(n – 1)
    n = log2 M where x , called the ceiling function, is the integer greater than or equal to x.
Example: How many bits are required to represent decimal digits with a binary code?
Notes: M = 10
Therefore n = 4 since:
24 =16 is  10 > 23 = 8
and the ceiling function for log2 10 is 4.

## Slide 54: Number of Elements Represented
Given n digits in radix r, there are rn distinct elements that can be represented.
But, you can represent m elements, m < rn
Examples:
  You can represent 4 elements in radix r = 2 with n = 2 digits: (00, 01, 10, 11).
  You can represent 4 elements in radix r = 2 with n = 4 digits: (0001, 0010, 0100, 1000).
  This second code is called a "one hot" code.

## Slide 55: Binary Codes for Decimal Digits
Decimal
8,4,2,1
Excess3
8,4,
-
2,
-
1
Gray
0
0000
0011
0000
0000
1
0001
0100
0111
0100
2
0010
0101
0110
0101
3
0011
0110
0101
0111
4
0100
0111
0100
0110
5
0101
1000
1011
0010
6
0110
1001
1010
0011
7
0111
1010
1001
0001
8
1000
1011
1000
1001
9
1001
1
100
1111
1000
There are over 8,000 ways that you can chose 10 elements from the 16 binary numbers of 4 bits. A few are useful:

## Slide 56: Binary Coded Decimal (BCD)
The BCD code is the 8,4,2,1 code.
This code is the simplest, most intuitive binary code for decimal digits and uses the same powers of 2 as a binary number, but only encodes the first ten values from 0 to 9.
Example: 1001 (9) = 1000 (8) + 0001 (1)
How many “invalid” code words are there?
What are the “invalid” code words?
Notes: Answer 1: 6
Answer 2: 1010, 1011, 1100, 1101, 1110, 1111

## Slide 57: Excess 3 Code and 8, 4, –2, –1 Code
What interesting property is common to these two codes?
Decimal | Excess 3 | 8, 4, –2, –1
0 | 0011 | 0000
1 | 0100 | 0111
2 | 0101 | 0110
3 | 0110 | 0101
4 | 0111 | 0100
5 | 1000 | 1011
6 | 1001 | 1010
7 | 1010 | 1001
8 | 1011 | 1000
9 | 1100 | 1111
Notes: Answer: Both of these codes have the property that the codes for 0 and 9, 1 and 8, etc. can be obtained from each other by replacing the 0’s with the 1’s and vice-versa in the code words. Such a code is sometimes called a complement code.

## Slide 58: GRAY CODE
Gray code is the arrangement of binary number system such that each incremental value can only differ by one bit.
This code is also known as Reflected Binary Code (RBC), Cyclic Code and Reflected Binary (RB). The reason for calling this code as reflected binary code is the first N/2 values compared with those of the last N/2 values in reverse order.
In gray code when transverse from one step to another step the only one bit will be change of the group. This means that the two adjacent code numbers differ from each other by only one bit.
It is popular for unit distance code but it is not use from arithmetic operations. This code has some application like convert analog to digital, error correction in digital communication.

## Slide 59: Binary- Gray code conversion
STEPS
  The most significant bit of gray code is equal to the first bit of the given binary bit.
  The second bit of gray code will be exclusive-or (XOR) of the first and second bit of the given binary bit.
  The third bit of gray code is equal to the exclusive-or (XOR) of the second and third binary bits. For father gray code result this process will be continuing.

## Slide 60: Explanation
The given binary digit is 01001
0 1 0 0 1 (Binary)
MSB
LSB
Gray code Conversion
0, 0 1, 1 0,0 0, 0 1
0 , 1 , 1 , 0 , 1 (On concatening)
The gray code of the given binary code (01001) =0 1 1 0 1 (One bit changed)
Truth Table of XOR |  | 
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 61: Example
The gray code of the given binary code is (010.01)2 ??
  The first MSB bit of binary is same in the first bit of gray code. In this example the binary bit is “0”. So, gray bit also “0”.
  Next gray bit is equal to the XOR of the first and the second binary bit. The first bit is 0, and the second bit is 1. The bits are different so resultant gray bit will be “1” (second gray codes bit)
  The XOR of the second and third binary bit. The second bit is 1 and third is 0. These bits are again different so the resultant gray bit will be 1 (third gray codes bit)
  Next we perform the XOR operation on third and fourth binary bit. The third bit is 0, and the fourth bit is 0. The both bits are same than resultant gray codes will be 0 (fourth gray codes bit).
  Take the XOR of the fourth and fifth binary bit. The fourth bit is 0 and fifth bit is 1. These bits are different than resultant gray codes will be 1 (fifth gray code bit)
  The result of binary to gray codes conversion is 01101.

## Slide 62: GRAY CODE TABLE The conversion in between decimal to gray and binary to gray code is given below
Decimal Number | Binary Number | Gray Code
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100
9 | 1001 | 1101
10 | 1010 | 1111
11 | 1011 | 1110
12 | 1100 | 1010
13 | 1101 | 1011
14 | 1110 | 1001
15 | 1111 | 1000
:
The gray code of the given binary code
(01001) =0 1 1 0 1. We can see one bit change in the next incremental value.

## Slide 63
You can convert n bit (bnb(n-1)…b2b1b0) binary number to gray code (gng(n-1)…g2g1g0). For most significant bit bn=gn, and rest of the bit by XORing b(n-1)=g(n-1)⊕gn, ….

## Slide 64: Explanation
The given gray code is 01101
0 1 1 0 1 (Gray)
MSB
LSB
Binary code Conversion
Truth Table of XOR |  | 
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 65: Gray-Binary code conversion
Steps
  The most significant bit of gray codes is equal in binary number.
  Now move to the next gray bit, as it is 1 the previous bit will be alter i.e it will be 1, thus the second binary bit will be 1.
  Next see the third bit, in this example the third bit is 1 again, the third binary bit will be alter of second binary bit and the third binary bit will be 0.
  Now fourth bit of the, here the fourth bit of gray code is 0. So the fourth bit will be same as a previous binary bit, i.e 4th binary bit will be 0.
  The last fifth bit of gray codes is 1; the fifth binary number is altering of fourth binary number.
  Therefore the gray code (01101) equivalent in binary number is (01001)

## Slide 66: Merits & Demerits of Gray Code
Advantages of gray code
It is best for error minimization in conversion of analog to digital signals.
It is best for minimize a logic circuit
Decreases the “Hamming Walls” which is undesirable state, when used in genetic algorithms
It is useful in clock domain crossing
Disadvantages of gray code
Not suitable for arithmetic operations
It has limited use.

## Slide 67: Decimal to BCD
Convert in BCD
From truth table the BCD value of
    So, =  (A)
    =
    On comparing (A) and (B) we understand that binary and BCD value of the given decimal is not same.

## Slide 68: Binary to BCD conversion
Step 1: Convert binary to decimal number
Step 2 : Convert decimal number to BCD
  Consider a binary number (11101)2 and convert it to BCD.
  Step 1: Convert binary to decimal number
  = ((
  Step 2 : Convert decimal number to BCD (in 4 digit) (Write the 4 digit BCD value for individual digit in decimal)
  =

## Slide 69: Advantages of BCD
  Easy to encode and Decode decimals into BCD and Vice-versa
  Easy to implement a hardware algorithm for BCD converter
  Very useful in digital systems whenever decimal information reqd.
  Digital voltmeters, frequency converters and digital clocks all use BCD as they display output information in decimal.

## Slide 70: Disadvantages of BCD Code
  Require more bits than straight binary code
  Difficult to be used in high speed digital computer when the size and capacity of their internal registers are restricted or limited.
  The arithmetic operations using BCD code require a complex design of Arithmetic and Logic Unit (ALU) than the straight binary number system.
  The speed of the arithmetic operations that can be realized using BCD code is naturally slow due to the complex hardware circuitry involved.

## Slide 71: Excess-3 code
The excess-3 code is also treated as XS-3 code. The excess-3 code is a non-weighted and self-complementary BCD code used to represent the decimal numbers.
This code has a biased representation. This code plays an important role in arithmetic operations because it resolves deficiencies encountered when we use the 8421 BCD code for adding two decimal digits whose sum is greater than 9.
The Excess-3 code uses a special type of algorithm, which differs from the binary positional number system or normal non-biased BCD.

## Slide 72: Decimal to Excess-3 code conversion
Step-1: We find the decimal number of the given binary number. Step-2: Then we add 3 in each digit of the decimal number.
Step-3: Now, we find the binary code of each digit of the newly generated decimal number.
Alternatively,
We can also add 0011 in each 4-bit BCD code of the decimal number for getting excess-3 code.

## Slide 73: Ex-1
Convert decimal Excess-3.
Step 1: Add ‘3’ to the given decimal  5+3=8
Step 2: Find binary digit of a new number ‘8’ which is
The Excess-3 code of given decimal is

## Slide 74: Ex-2
Convert BCD Excess-3.
Step 1: Add BCD value of 3 (0011) to the given number.
0 1 0 1
0 0 1 1(+)
1 0 0 0
=

## Slide 75: Ex-3
Convert decimal Excess-3.
Step 1: Add ‘3’ to the individual given decimal
The Excess-3 code of given decimal is

## Slide 76: Excess-3 code

## Slide 77: Ex-4
Convert decimal Excess-3.
Step 1: Step 2:
Decimal
BCD
Decimal | BCD
8 | 1000
1 | 0001
6 | 0110
1 | 0001
BCD+ 0011 | Excess-3
1000+0011 | 1011
0001+0011 | 0100
0110+0011 | 1001
0001+0011 | 0100

## Slide 78: Ex 5
Convert (11110)2 to Excess-3 using binary
Step 1: Convert binary to Decimal. (11110)2 = (30)10
Step 2: Add ‘3’ to individual digits to decimal number
3 0
3 3
6 3
Step 3: Find binary values of (63)10 = (01100011)Excess-3

## Slide 79: Ex 6
Convert (01100011) Excess-3 to binary.
Step- 1 : Find the decimal by dividing it four digits
  (01100011) Excess-3 = (0110 0011) Excess-3 = (30) 10
Step-2 : Find the binary value of the decimal thorugh division method.
(01100011) Excess-3 = (11110)2

## Slide 80: Advantages
These codes are self-complementary.
These codes use biased representation.
The excess-3 code has no limitation, so that it considerably simplifies arithmetic operations.
The codes 0000 and 1111 can cause a fault in the transmission line. The excess-3 code doesn't use these codes and gives an advantage for memory organization.
These codes are usually unweighted binary decimal codes.
This code has a vital role in arithmetic operations. It is because it resolves deficiencies which are encountered when we use the 8421 BCD code for adding two decimal digits whose sum is greater than 9.

## Slide 81: ASCII
The ASCII stands for American Standard Code for Information Interchange. The ASCII code is an alphanumeric code used for data communication in digital computers.
The ASCII is a 7-bit code capable of representing 27 or 128 number of different characters. The ASCII code is made up of a three-bit group, which is followed by a four-bit code.

## Slide 82: ASCII Characters
Control Characters-0 to 31 and 127
Special Characters- 32 to 47, 58 to 64, 91 to 96, and 123 to 126
Numbers Characters- 0 to 9
Letters Characters - 65 to 90 and 97 to 122
ASCII Character Set

## Slide 83: Ex 1
Encode (10010101100001111011011000011010100111000011011111101001 110111011101001000000011000101100100110011)2 to ASCII.

## Slide 84
Step 1:
The given binary data is grouped into 7-bits because the ASCII code is 7 bit.
1001010 1100001 1110110 1100001 1010100 1110000 1101111 1101001 1101110 1110100 1000000 0110001 0110010 0110011
Step 2:
Then, we find the equivalent decimal number of the binary digits either from the ASCII table or 64 32 16 8 4 2 1 scheme.

## Slide 85: Cont’d
Binary | 64 | 32 | 16 | 8 | 4 | 2 | 1 | DECIMAL | ASCII
1100011 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 99 | C
1101111 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 111 | O
1101101 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 109 | M
1110000 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 112 | P
1110101 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 117 | U
1110100 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 116 | T
1100101 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 101 | E
1110010 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 114 | R
So the given binary digits results in ASCII Keyword COMPUTER

## Slide 86: Parity Code
The parity code is used for the purpose of detecting errors during the transmission of binary information. The parity code is a bit that is included with the binary data to be transmitted.
The inclusion of a parity bit will make the number of 1’s either odd or even. Based on the number of 1’s in the transmitted data, the parity code is of two types.
  Even parity code
  Odd parity code

## Slide 87
In even parity, the added parity bit will make the total number of 1’s an even number.
If the added parity bit make the total number of 1’s as odd number, such parity code is said to be odd parity code.

## Slide 88: Explanation

## Slide 89
On the receiver side, if the received data is other than the sent data, then it is an error. If the sent date is even parity code and the received data is odd parity, then there is an error.
So, both even and odd parity codes are used only for the detection of error and not for the correction in the transmitted data. Even parity is commonly used and it has almost become a convention.

## Slide 90
Advantages
  Easy to implement
  Simple method
  Used error detection
Demerits
  No error correction

## Slide 91: Warning: Conversion or Coding?
Do NOT mix up conversion of a decimal number to a binary number with coding a decimal number with a BINARY CODE.
1310 = 11012 (This is conversion)
13  0001|0011 (This is coding)

## Slide 92: Binary Arithmetic
Single Bit Addition with Carry
Multiple Bit Addition
Single Bit Subtraction with Borrow
Multiple Bit Subtraction
Multiplication
BCD Addition

## Slide 93: Multiple Bit Binary Addition
Extending this to two multiple bit examples:
Carries 0 0
Augend 01100 10110
Addend +10001 +10111
Sum
Note: The 0 is the default Carry-In to the least significant bit.
Notes: Carries 00000 01100
Augend 01100 10110
Addend +10001 +10111
Sum 11101 101101

## Slide 94: Single Bit Binary Subtraction with Borrow
Given two binary digits (X,Y), a borrow in (Z) we get the following difference (S) and borrow (B):
Borrow in (Z) of 0:
Borrow in (Z) of 1:
Z
1
1
1
1
X
0
0
1
1
- Y
-0
-1
-0
-1
BS
11
1 0
0 0
1 1
Z
0
0
0
0
X
0
0
1
1
- Y
-0
-1
-0
-1
BS
0 0
1 1
0 1
0 0

## Slide 95: Multiple Bit Binary Subtraction
Extending this to two multiple bit examples:
Borrows 0 0
Minuend 10110 10110
Subtrahend - 10010 - 10011
Difference
Notes: The 0 is a Borrow-In to the least significant bit. If the Subtrahend > the Minuend, interchange and append a – to the result.
Notes: Borrows 00000 00110
Minuend 10110 10110
Subtrahend –10010 –10011
Difference 00100 00011

## Slide 96: Number System

## Slide 97: Octal Number System
Octal to Binary
Octal to Decimal
Octal to Hexadecimal

## Slide 98: Octal to Binary
Octal number is one of the number systems which has value of base is 8, that means there only 8 symbols − 0, 1, 2, 3, 4, 5, 6, and 7.
Whereas Binary number is most familiar number system to the digital systems, networking, and computer professionals.

## Slide 99: Octal to Binary Equivalent Table

## Slide 100: Octal to Binary
This method is simple and also works as reverse of Binary to Octal Conversion. The algorithm is explained as following below.
Take Octal number as input
Convert each digit of octal into binary.
That will be output as binary number.

## Slide 101: Octal to Binary
Example-1 Convert octal number 25 into binary number.

## Slide 102: Octal to Binary
Example-2 Convert octal number 540 into binary number.
According to above algorithm, equivalent binary number will be,
= (540)8 = (101 100 000)2 = (101100000)2

## Slide 103: Octal to Binary
Example 3: Convert octal number 12.5 & 721 into binary number.

## Slide 104: Octal to Binary
Example 4: Convert octal number 352.563 into binary number.
According to above algorithm, equivalent binary number will be,
= (352.563)8 = (011 101 010 . 101 110 011)2 = (011101010.101110011)2

## Slide 105: Octal to Decimal
To convert an octal number to a decimal number we need to multiply each digit of the given octal with the reducing power of 8.
Let us learn here, the conversion of Octal number to Decimal Number or base 8 to base 10.

## Slide 106: Octal to Decimal
Example 1: Convert octal number 37246(8) into decimal form.

## Slide 107: Octal to Decimal
Example 2: Convert octal number 1725.43(8) into decimal form.

## Slide 108: Octal to Decimal
Example 3: Convert octal number 7.12172(8) into decimal form.
= 7x80 + 1x8-1 + 2x8-2 + 1x8-3 + 7x8-4 + 2x8-5
= 7 + 0.125 + 0.03125 + 0.001953125 + 0.001708984375 + 0.00006103515624
= 10.1599

## Slide 109: Octal to Hexadecimal
First turning the octal number into a
1. Binary Digit
2. binary to Hexadecimal

## Slide 110: Octal to Hexadecimal

## Slide 111: Octal to Hexadecimal
Example 1: Convert octal number 5456 (8) into hexadecimal form.

## Slide 112: Octal to Hexadecimal
Example 2: Convert octal number 343.405(8) into hexadecimal form.

## Slide 113: Hexadecimal Number System
Hexadecimal to Binary
Hexadecimal to decimal
Hexadecimal to octal

## Slide 114: Hexadecimal to Binary
Example 1: Convert hexadecimal number BAB2 (16) into binary form.

## Slide 115: Hexadecimal to Binary
Example 2: Convert hexadecimal number CD4.28C (16) into binary form.

## Slide 116: Hexadecimal to decimal
Example 1: Convert hexadecimal number 1AB (16) into decimal form.

## Slide 117: Hexadecimal to decimal
Example 2: Convert hexadecimal number 54.D2 (16) into decimal form.

## Slide 118: Hexadecimal to octal
First turning the hexadecimal number into a
1. Binary Number
2. binary to octal

## Slide 119: Hexadecimal to octal
Example 1: Convert hexadecimal number A4B.59E (16) into decimal form.

## Slide 120: Signed Binary Numbers
Two ways of representing signed numbers:
  1) Sign-magnitude form, 2) Complement form.
Most of computers use complement form for negative number notation.
1’s complement and 2’s complement are two different methods in this type.

## Slide 121: 1’s Complement
1’s complement of a binary number is obtained by subtracting each digit of that binary number from 1.
Example
Shortcut: Invert the numbers from 0 to 1 and 1 to 0

## Slide 122: 2’s Complement
2’s complement of a binary number is obtained by adding 1 to its 1’s complement.
Example
Shortcut: Starting from right side, all bits are same till first 1 occurs and then invert rest of the bits

## Slide 123: Subtraction using 1’s complement
Using 1’s complement
  Obtain 1’s complement of subtrahend
  Add the result to minuend and call it intermediate result
  If carry is generated then answer is positive and add the carry to Least Significant Digit (LSD)
  If there is no carry then answer is negative and take 1’s complement of intermediate result and place negative sign to the result.

## Slide 124: Subtraction using 2’s complement
Using 2’s complement
  Obtain 2’s complement of subtrahend
  Add the result to minuend
  If carry is generated then answer is positive, ignore carry and result itself is answer
  If there is no carry then answer is negative and take 2’s complement of intermediate result and place negative sign to the result.

## Slide 125: Subtraction using 1’s complement (Examples)
Example - 1

## Slide 126: Subtraction using 1’s complement (Examples)
Example - 2

## Slide 127: Subtraction using 2’s complement (Examples)
Example - 1

## Slide 128: Subtraction using 2’s complement (Examples)
Example - 2

## Slide 129: BCD ARITHMETIC

## Slide 130: BCD Addition
Example - 1
Rule: If there is an illegal code or carry is generated as a result of addition, then add 0110 to particular that 4 bits of result.

## Slide 131: BCD Addition
Example - 2

## Slide 132: BCD Subtraction
Example - 1
Rule: If one 4-bit group needs to take borrow from neighbor, then subtract 0110 from the group which is receiving borrow.

## Slide 133: BCD Subtraction
Example - 2

## Slide 134: Logic Gates
Goal:
To understand how digital a computer can work, at the lowest level.
To understand what is possible and the limitations of what is possible for a digital computer.

## Slide 135: Logic Gates
All digital computers for the past 50 years have been constructed using the same type of components.
These components are called logic gates.
Logic gates have been implemented in many different ways.
Currently, logic gates are most commonly implemented using electronic VLSI transistor logic.

## Slide 136: Logic Gates
A logic gate is a simple switching circuit that determines whether an input pulse can pass through to the output in digital circuits.
The building blocks of a digital circuit are logic gates, which execute numerous logical operations that are required by any digital circuit.
These can take two or more inputs but only produce one output.
The mix of inputs applied across a logic gate determines its output. Logic gates use Boolean algebra to execute logical processes.
Logic gates are found in nearly every digital gadget we use on a regular basis.
Logic gates are used in the architecture of our telephones, laptops, tablets, and memory devices.

## Slide 137
All basic logic gates have the ability to accept either one or two input signals (depending upon the type of gate) and generate one output signal.
Logic Gates

## Slide 138: Boolean Algebra
Boolean algebra is a type of logical algebra in which symbols represent logic levels.
The digits(or symbols) 1 and 0 are related to the logic levels in this algebra; in electrical circuits, logic 1 will represent a closed switch, a high voltage, or a device’s “on” state.
An open switch, low voltage, or “off” state of the device will be represented by logic 0.
At any one time, a digital device will be in one of these two binary situations. A light bulb can be used to demonstrate the operation of a logic gate.
When logic 0 is supplied to the switch, it is turned off, and the bulb does not light up.
The switch is in an ON state when logic 1 is applied, and the bulb would light up.
In integrated circuits (IC), logic gates are widely employed.

## Slide 139
Input and Output signals are binary.
    binary:
      always in one of two possible states;
      typically treated as:
        On / Off (electrically)
        1 / 0
        True / False
There is a delay between when a change happens at a logic gates inputs and when the output changes, called gate switching time.
The True or False view is most useful for thinking about the meaning of the basic logic gates.

## Slide 140: Truth Table
The outputs for all conceivable combinations of inputs that may be applied to a logic gate or circuit are listed in a truth table.
When we enter values into a truth table, we usually express them as 1 or 0, with 1 denoting True logic and 0 denoting False logic.

## Slide 141: Classification

## Slide 142
Basic Logic Gates-
Basic Logic Gates are the fundamental logic gates using which universal logic gates and other logic gates are constructed.
They have the following properties-
Basic logic gates are associative in nature.
Basic logic gates are commutative in nature.
There are following three basic logic gates-
AND Gate
OR Gate
NOT Gate

## Slide 143: AND gate
The output of AND gate is high (‘1’) if all of its inputs are high (‘1’).
The output of AND gate is low (‘0’) if any one of its inputs is low (‘0’).

## Slide 144: Logic Symbol

## Slide 145: Truth Table

## Slide 146: OR Gate
The output of OR gate is high (‘1’) if any one of its inputs is high (‘1’).
The output of OR gate is low (‘0’) if all of its inputs are low (‘0’).

## Slide 147: Logic Symbol
Logic Symbol-
The logic symbol for OR Gate is as shown below-

## Slide 148: Truth Table

## Slide 149: NOT Gate
The output of NOT gate is high (‘1’) if its input is low (‘0’).
The output of NOT gate is low (‘0’) if its input is high (‘1’).
From here-
It is clear that NOT gate simply inverts the given input.
Since NOT gate simply inverts the given input, therefore it is also known as Inverter Gate.

## Slide 150
Logic Symbol-
The logic symbol for NOT Gate is as shown below-

## Slide 152: Universal Logic Gates
Universal logic gates are the logic gates that are capable of implementing any Boolean function without requiring any other type of gate.
They are called as “Universal Gates” because-
They can realize all the binary operations.
All the basic logic gates can be derived from them.
They have the following properties-
Universal gates are not associative in nature.
Universal gates are commutative in nature.

## Slide 153
A NAND Gate is constructed by connecting a NOT Gate at the output terminal of the AND Gate.
The output of NAND gate is high (‘1’) if at least one of its inputs is low (‘0’).
The output of NAND gate is low (‘0’) if all of its inputs are high (‘1’).

## Slide 156: NOR Gate
A NOR Gate is constructed by connecting a NOT Gate at the output terminal of the OR Gate.
The output of OR gate is high (‘1’) if all of its inputs are low (‘0’).
The output of OR gate is low (‘0’) if any of its inputs is high (‘1’).

## Slide 158: Truth Table

## Slide 159: EX-OR & EX-NOR Gates
One of the inputs of alternative gate will have a bubble (which represents NOT gate).
For EX-OR structured original gate, alternative gate will be EX-NOR structured.
For EX-NOR structured original gate, alternative gate will be EX-OR structured.
If bubble is present at the output of original gate, then no bubble will be present at the output of alternative gate.
If bubble is not present at the output of original gate, then a bubble will be present at the output of alternative gate.

## Slide 160: Example
1.Q = A AND (B AND C)
Step 1 – Start with the brackets, this is the “B AND C” part.
Step 2 – Add the outer expression, this is the “A AND” part.

## Slide 161: Example
2.Q = NOT (A OR B)
Step 1 – Start with the brackets, this is the “A OR B” part
Step 2 – Add the outer expression, this is the “NOT” part.